## Slide 1
VIRTUALIZATION & CLOUD COMPUTING | UNIT 1
Computer Networks
Networking Foundations for Virtualization & Cloud Computing – Unit 1
By Soni Bhambar

## Slide 2
Topics to be Covered
1. Introduction to Computer Networks
Definition, uses, components & topologies
2. Network Models
Why layered architectures are used
3. OSI Model & TCP/IP Model
Layers, functions and comparison
4. The Internet
Structure, IP addressing and DNS
5. Protocols
Rules that govern communication
6. Network Applications
Real-world uses, incl. Cloud & Virtualization
Virtualization & Cloud Computing · Unit 1
2

## Slide 3
INTRODUCTION
What Is a Computer Network?
A collection of interconnected computing devices (computers, servers, mobile devices) that can exchange data and share resources using a common communication medium and set of rules.
Devices are called nodes or hosts
Connected via wired links (cable, fibre) or wireless links (radio, Wi-Fi)
Enables sharing of data, hardware and applications
Governed by a set of rules called protocols
Desktop
Laptop
Mobile
Server
Virtualization & Cloud Computing · Unit 1
3

## Slide 4
INTRODUCTION
Why Computer Networks Matter
Resource Sharing
Share printers, storage, software and internet access across users.
Communication
Email, messaging and video calls connect people instantly, anywhere.
Centralised Data
Store and manage data centrally for consistency and easy backup.
Scalability & Cost
Add users or services incrementally; reduce hardware duplication.
Virtualization & Cloud Computing · Unit 1
4

## Slide 5
INTRODUCTION
Core Components of a Network
Node / Host
Any device that sends or receives data — computers, servers, phones, printers.
Link (Medium)
The physical or wireless path data travels through — cable, fibre optic, radio waves.
Switch / Router
Intermediate devices that direct data to its correct destination.
Network Interface Card (NIC)
Hardware that connects a device to the network medium.
Protocol
Agreed rules that define how data is formatted, sent and received.
Virtualization & Cloud Computing · Unit 1
5

## Slide 6
INTRODUCTION
Types of Networks by Geographic Scale
PAN
Personal Area Network
Range: ~10 m
Bluetooth headset, smartwatch
LAN
Local Area Network
Range: Building / Campus
Office or college network
MAN
Metropolitan Area Network
Range: A city
Cable TV network, city Wi-Fi
WAN
Wide Area Network
Range: Country / Global
The Internet itself
Virtualization & Cloud Computing · Unit 1
6

## Slide 7
Feature | PAN (Personal) | LAN (Local) | MAN (Metropolitan) | WAN (Wide)
Full Name | Personal Area Network | Local Area Network | Metropolitan Area Network | Wide Area Network
Geographic Range | Within 10 meters (33 ft) | Under 1 kilometer (0.6 miles) | 5 to 50 kilometers | Global / Country-wide
Primary Use Case | Connecting personal gadgets | Connecting a single building | Connecting a whole city | Connecting continents
Data Speed | Moderate (up to 24 Mbps) | Very High (up to 10 Gbps) | High (up to 1 Gbps) | Lower (varies by region)
Common Technology | Bluetooth, Zigbee | Ethernet, Wi-Fi | Fiber-optic, Microwave | Leased lines, Satellite
Ownership | Single individual | Single private organization | Joint / Telecom company | Multiple organizations
Setup Cost | Very low | Low to moderate | High | Very high
Error Rates | Very low | Low | Moderate | High
Comparison of Types of Networks

## Slide 8
INTRODUCTION
Network Topologies
Star
All nodes connect to a central hub
Bus
All nodes share one common cable
Ring
Nodes form a closed loop
Mesh
Every node connects to every other
Virtualization & Cloud Computing · Unit 1
7

## Slide 9
INTRODUCTION
Client–Server vs Peer-to-Peer (P2P)
Client–Server
A dedicated server provides resources/services
Clients request data or services from the server
Centralised control, easier security & backup
Example: Web servers, email servers, databases
Peer-to-Peer (P2P)
Every device (peer) acts as both client and server
Peers share resources directly with each other
No central point of control; more fault-tolerant
Example: File-sharing networks, blockchain nodes
Virtualization & Cloud Computing · Unit 1
8

## Slide 10
SECTION 02
Network Models
Understanding layered architecture in computer networks

## Slide 11
NETWORK MODELS
Why We Use Layered Network Models
Network communication is broken into independent layers, each handling one specific job. This is called a layered architecture.
Modularity
Each layer is designed and updated independently without affecting others.
Simplifies Design
Complex networking tasks are broken into smaller, manageable problems.
Interoperability
Devices from different vendors can communicate using standard layers.
Easier Troubleshooting
Faults can be isolated to a specific layer rather than the whole system.
Virtualization & Cloud Computing · Unit 1
10

## Slide 12
NETWORK MODELS
The OSI Model — 7 Layers
7
Application
Interfaces directly with end-user software
6
Presentation
Data translation, encryption, compression
5
Session
Establishes & manages sessions between hosts
4
Transport
Reliable end-to-end delivery (TCP/UDP)
3
Network
Logical addressing & routing (IP)
2
Data Link
Physical addressing, framing (MAC)
1
Physical
Transmission of raw bits over medium
Memory Aid
“All People Seem To Need Data Processing”
Layers 7 → 1: Application, Presentation, Session, Transport, Network, Data Link, Physical
Developed by ISO as a conceptual reference model — it is not implemented directly, but used to understand and design network communication.
Virtualization & Cloud Computing · Unit 1
11

## Slide 13
NETWORK MODELS
OSI Model — Layer Functions & Examples
# | Layer | Key Function | Examples / PDU
7 | Application | User-facing services & network access | HTTP, FTP, SMTP · Data
6 | Presentation | Data format, encryption, compression | SSL/TLS, JPEG, ASCII
5 | Session | Opens, manages & closes sessions | NetBIOS, RPC
4 | Transport | Reliable/unreliable end-to-end delivery | TCP, UDP · Segments
3 | Network | Logical addressing & path selection | IP, ICMP · Packets
2 | Data Link | Node-to-node delivery, error detection | Ethernet, MAC · Frames
1 | Physical | Bit transmission over physical medium | Cables, Hubs · Bits
Virtualization & Cloud Computing · Unit 1
12

## Slide 14
NETWORK MODELS
The TCP/IP Model — 4 Layers
A practical, implementation-based model that the modern Internet is actually built on — developed by the US DoD before OSI.
Application
Combines OSI's Application, Presentation & Session layers
HTTP, FTP, SMTP, DNS
Transport
End-to-end communication & reliability
TCP, UDP
Internet
Logical addressing & routing across networks
IP, ICMP, ARP
Network Access
Combines OSI's Data Link & Physical layers
Ethernet, Wi-Fi
Virtualization & Cloud Computing · Unit 1
13

## Slide 15
NETWORK MODELS
OSI vs TCP/IP — Side-by-Side Comparison
OSI MODEL (7)
TCP/IP MODEL (4)
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Internet
Network Access
Virtualization & Cloud Computing · Unit 1
14

## Slide 16
SECTION 03
The Internet
A global network of interconnected networks

## Slide 17
THE INTERNET
What Is the Internet & How Is It Structured?
The Internet is a vast, global “network of networks” that connects billions of devices worldwide using the standardised TCP/IP protocol suite.
ISPs (Internet Service Providers)
Provide access by connecting homes/organisations to the Internet backbone
Backbone Networks
High-capacity fibre links that carry data between major regions globally
Routers & Exchange Points
Direct traffic efficiently between thousands of interconnected networks
You
Local ISP
Internet Backbone
Destination ISP
Web Server
Virtualization & Cloud Computing · Unit 1
16

## Slide 18
THE INTERNET
IP Addressing — IPv4 vs IPv6
Every device on a network needs a unique IP address to send and receive data — like a postal address for the digital world.
IPv4
32-bit
192.168.1.1
~4.3 billion unique addresses
Written as 4 decimal numbers (0-255)
Address exhaustion due to device growth
IPv6
128-bit
2001:0db8::1
3.4 × 10³⁸ unique addresses
Written in 8 groups of hexadecimal
Designed to solve IPv4 exhaustion
Virtualization & Cloud Computing · Unit 1
17

## Slide 19
THE INTERNET
Domain Name System (DNS)
DNS translates human-friendly domain names into the numeric IP addresses computers use to identify each other — often called the “phonebook of the Internet.”
User types
www.example.com
DNS Resolver
Looks up the domain
DNS Server
Returns matching IP
Web Server
192.0.2.10 responds
Virtualization & Cloud Computing · Unit 1
18

## Slide 20
SECTION 04
Protocols
The rules that make network communication possible

## Slide 21
PROTOCOLS
What Is a Network Protocol?
A protocol is a formal set of rules and conventions that governs how devices communicate, format, transmit and interpret data over a network.
Syntax
The structure or format of the data — how bits are organised into fields.
Semantics
The meaning of each field — what action or response it indicates.
Timing
When data should be sent and at what speed it should arrive.
Virtualization & Cloud Computing · Unit 1
20

## Slide 22
PROTOCOLS
Key Network Protocols
HTTP / HTTPS
Transfers web pages; HTTPS adds encryption
FTP
Transfers files between client and server
SMTP
Sends email between mail servers
DNS
Resolves domain names to IP addresses
TCP
Reliable, connection-oriented data delivery
UDP
Fast, connectionless data delivery
IP
Addresses and routes packets across networks
SSH
Secure remote login and command execution
Virtualization & Cloud Computing · Unit 1
21

## Slide 23
PROTOCOLS
TCP vs UDP — Transport Layer Comparison
 | TCP | UDP
Connection | Connection-oriented (handshake) | Connectionless
Reliability | Guaranteed delivery, error checking | No delivery guarantee
Ordering | Data arrives in order | Order not guaranteed
Speed | Slower due to overhead | Faster, minimal overhead
Use Cases | Web, email, file transfer | Video streaming, gaming, VoIP
Virtualization & Cloud Computing · Unit 1
22

## Slide 24
SECTION 05
Network Applications
How networks power everyday digital services

## Slide 25
NETWORK APPLICATIONS
Everyday Applications Built on Networks
Web Browsing
Access websites via HTTP/HTTPS
Email
Send & receive messages via SMTP/IMAP
File Transfer
Upload/download files via FTP
Video Conferencing
Real-time audio/video calls
Cloud Computing
Remote storage & computing power
IoT Devices
Smart devices sharing sensor data
Social Media
Content sharing & messaging platforms
Streaming
On-demand audio & video delivery
Virtualization & Cloud Computing · Unit 1
24

## Slide 26
NETWORK APPLICATIONS
Why Networking Matters for Virtualization & Cloud
Virtual Machine Connectivity
Virtual switches & NICs let VMs on the same host or across hosts communicate.
Cloud Service Delivery
IaaS, PaaS & SaaS are all delivered to users entirely over the network.
Distributed & Shared Storage
SAN/NAS and cloud storage are accessed remotely by virtualized workloads.
Virtual Networks & VLANs
Software-defined networking isolates and connects VMs across data centres.
Load Balancing & Scaling
Traffic is routed across VM/container instances to scale cloud applications.
APIs for Cloud Management
Provisioning and orchestration tools (e.g. hypervisor/cloud APIs) run over HTTP.
Virtualization & Cloud Computing · Unit 1
25

## Slide 27
SUMMARY
Key Takeaways
1
A computer network connects devices to share resources and communicate using protocols.
2
Layered models (OSI's 7 layers, TCP/IP's 4 layers) organise networking tasks into manageable, standard stages.
3
The Internet is a global network of networks, relying on IP addressing and DNS for identification.
4
Protocols are the agreed rules — HTTP, TCP, UDP, DNS and more — that make reliable communication possible.
5
Network applications from web browsing to cloud computing and IoT power everyday life and modern data science workflows.
Virtualization & Cloud Computing · Unit 1
26

## Slide 28
Thank You
Questions & Discussion
Virtualization & Cloud Computing · Unit 1 · Networking Foundations